Use at your own risk. The pilot must refer to the FAA approved documents for the correct information, and is responsible for safe operation of aircraft.

| Cessna 152 v1.7 |
| --- |
| BEFORE TAKEOFF: Clearing circle for Pattern Traffic What is your ABORT Plan? ( Flaps UP or 10° ( Carb Heat OFF ( Transponder ALT ( Lights/Strobes ON ( Headset ON |
| TAKEOFF Normal: Rotate 50 kts Vy 67 kts (61 kts @ 10,000’) Short/Soft: Flaps 10° Vx 54 kts (59 kts @ 10,000’) |
| CRUISE CLIMB 70-80 kts BEST GLIDE 60 kts (flaps up) |
| >1000’ AGL ( Oil Pres/Temp ( Ammeter ( Vacuum |
| CRUISE ( Max 75% power ( Mixture LEAN for max RPM ( Heading Indicator SET ( Routinely Check Gauges: ( Oil Press/Temp ( Ammeter ( Vacuum ( Fuel ( Landing Light OFF |
| LANDING ( Carb Heat ON ( Mixture ENRICH Approach at 55-65 kts |
| GO AROUND ( Full Throttle ( Pitch up ( Carb Heat OFF ( Flaps retract to 20° ( Climbing & above 55 kts retract flaps |
| AFTER LANDING ( Carb Heat OFF ( Transponder SBY ( Flaps UP ( Mixture LEAN for taxi |
| SHUTDOWN ( Avionics/Lights OFF ( Mixture OFF ( Master OFF ( Mags OFF ( Headset OFF ( Flight Plan CLOSED ( Control Lock INSTALLED |
| POSTFLIGHT ( Hobbs Time RECORD ( Windows & Leading Edges CLEAN ( Wheel Chocks SET ( Seat Belts SECURE ( Interior CLEAN ( Airplane LOCKED ( Flight Log ENTERED ( Flight Plan CLOSED ( Hangar SECURE ( Padlock Set 0000 ( Lights OFF |
| CAS KTS Vso 35 Vs1 40 Vfe 85 Va 1670 104 Va 1500 98 Va 1350 93 Vno 111 Vne 149 | Recommended Pattern Speeds/ Approx Pwr Settings Downwind : 80 - 85 Kts 2000 RPM Abeam: 70 - 75 Kts 1500 RPM Base: 65 - 70 Kts 1500 RPM Final: 55 - 60 Kts 1500 RPM (Full Flaps – No Flaps) |

Use at your own risk. The pilot must refer to the FAA approved documents for the correct information, and is responsible for safe operation of aircraft.

| Cessna 152 v1.7 |
| --- |
| PREFLIGHT Gust Lock - REMOVED Hobbs – Recorded. Enter flight into Flight Log System Master – ON Flaps – 20° Fuel Gauges – CHECK Exterior Lights - CHECK Interior Lights - CHECK Master – OFF Tires/Brakes – Press/Leaks (Main 21 psi - Nose 30 psi) Fuel Caps & Quantity Fuel Vents Oil level: 4 MIN / 5 MAX Qts. Nose strut Static Port Wing Fuel Drains Engine Fuel Strainer START Seats – LOCKED Seat Belts – FASTEN Brakes – SET Passenger Briefing Fuel – ON Circuit Breakers – IN Avionics – OFF Mixture – RICH Carb Heat – COLD Prime – As Required (max 3) Throttle – Open ½ Inch Clear Prop Master–ON, Electronic Mag -ON Engage Starter - (max 20 sec crank if no start) Make sure Electronic Mag Switch is ON | AFTER START Throttle – 1000 RPM Oil Pressure– in green < 30 seconds Flaps – UP Mixture – LEAN FOR TAXI Avionics – ON Beacon – ON Nav Lights – As Required Transponder – STBY RUNUP Doors & Windows – LATCHED Controls – FREE & CORRECT Flaps – UP Trim – TAKEOFF Fuel – ON Throttle – 1700 RPM Mixture – BEST POWER Vacuum – Check (4.6”-5.4”) MAG TEST: Note: Electronic Ignition on L mag. Drop will be different (R < 150 rpm, L < 50 rpm) When switching R to Both there will be a slight loss of power, this is normal. Switch mag positions quickly to minimize momentary loss of power. Carb Heat – TEST Alternator – TEST Throttle – 1000 RPM Instruments – CHECK Seat Belts – CHECK COM – First Freqs 122.7 KMAN NAV – First Freqs OBS – SET Charts & Log – READY Headset – ON SEE OTHER SIDE FOR BEFORE TAKEOFF CHECK |
| Emergency: Com 121.5 / Squawk 7700 Loss Com. Squawk 7600 Flight Watch: 122.0 FSS BOI: 122.2 / 122.6 KMAN ASOS:118.325 KEUL ASOS :135.07 KBOI ATIS:123.9 Big Sky App/Dep: North 126.9 / South 119.6 BOI Twr 118.1 / Gnd 121.7 |