Use at your own risk. The pilot must refer to the FAA approved documents for the correct information, and is responsible for safe operation of aircraft.

| Cessna 172M – 160HP V1.2 |
| --- |
| BEFORE TAKEOFF - Clearing circle for Pattern Traffic ( What is your ABORT Plan? ( Flaps UP ( Carb Heat OFF ( Transponder ALT ( Lights/Strobes ON ( Headset ON |
| TAKEOFF Normal: Rotate 60 mph Vy 91 mph (80 mph @ 10,000’ DA) Short/Soft: Flaps 0 /10° Vx 68 mph (73 mph @ 10,000’ DA) |
| CRUISE CLIMB 90 mph RPM Do Not exceed 2500 RPM for more than 5 min during climb out BEST GLIDE 80 mph (flaps up) |
| >1000’ AGL ( Oil Pres/Temp ( Ammeter ( Vacuum ( Lights |
| CRUISE Do Not exceed 2500 RPM for more than 5 min during Cruse ( Landing Light OFF ( Mixture LEAN for max RPM ( Heading Indicator SET ( Routinely Check Gauges: ( Oil Press/Temp ( Ammeter ( Vacuum ( Fuel ( Carb Temp (64R) |
| LANDING ( Carb Heat ON ( Fuel BOTH ( Mixture ENRICH ( Approach at 65-75 mph |
| GO AROUND ( Full Throttle ( Pitch up ( Carb Heat OFF ( Flaps retract to 20° ( Climbing & above 65 mph retract flaps |
| AFTER LANDING ( Carb Heat OFF ( Transponder SBY ( Flaps UP ( Mixture LEAN for taxi |
| SHUTDOWN ( Avionics/Lights OFF ( Mixture OFF ( Master OFF ( ( Mags OFF ( Headset OFF ( Parking Brake SET ( Control Lock Installed ( Flight Plan Closed |
| POSTFLIGHT ( Hobbs Time RECORD ( Windows & Leading Edges CLEAN ( Wheel Chocks SET ( Seat Belts SECURE ( Interior CLEAN ( Airplane LOCKED ( Flight Log ENTERED ( Flight Plan CLOSED ( Hangar SECURE ( Padlock Set 0000 ( Lights OFF |
| CAS MPH Vso 54 Vs1 61 Vfe 100 Va 2300 112 Va 1950 103 Va 1600 93 Vno 145 Vne 182 | Recommended Pattern Speeds/ Approx Pwr Settings Downwind: 90 - 95 mph / 2000 RPM Abeam: 80 - 85 mph / 1500 RPM Base: 75 - 80 mph / 1500 RPM Final: 65 - 70 mph / 1500 RPM (Full Flaps – No Flaps) |

Use at your own risk. The pilot must refer to the FAA approved documents for the correct information, and is responsible for safe operation of aircraft.

| Cessna 172M – 160HP V1.2 |
| --- |
| PREFLIGHT Gust Lock - REMOVED Hobbs – Recorded. Enter flight into Flight Log System Master – ON Flaps – 20° Fuel Gauges – CHECK Exterior Lights - CHECK Interior Lights - CHECK Master – OFF Baggage Door – LOCKED Tires/Brakes – Press/Leaks (Main 29 psi - Nose 31 psi) Fuel Caps & Quantity Fuel Vents Oil level: 6 MIN / 7 MAX Qts. Nose strut Static Port Wing Fuel Drains Engine Fuel Strainer START Seats – LOCKED Selt Belts – FASTEN Parking Brake – SET Passenger Briefing Fuel – BOTH Circuit Breakers – IN Avionics – OFF Mixture – RICH Carb Heat – COLD Prime – As Required Throttle – OPEN ½ Inch Clear Prop Master – ON Engage Starter (max 20 sec crank if no start) Release when engine starts. | AFTER START Throttle – 1000 RPM Oil Pressure– in green < 30 seconds Flaps – UP Mixture – LEAN FOR TAXI Avionics – ON Beacon – ON Nav Lights – As Required Transponder – STBY RUNUP Doors & Windows – LATCHED Controls – Free & Correct Flaps – UP Trim – TAKEOFF Fuel – BOTH Throttle – 1700 RPM Mixture – BEST POWER Vacuum – Check (4.6”-5.4”) Mags (drop< 125, difference ea <50) Carb Heat – TEST Alternator – TEST Throttle – 1000 RPM Instruments – CHECK Seat Belts – CHECK COM – First Freqs 122.7 KMAN NAV – First Freqs OBS – SET Charts & Log – READY Headset – ON SEE OTHER SIDE FOR BEFORE TAKEOFF CHECK |
| Emergency: Com 121.5 / Squawk 7700 Loss Com. Squawk 7600 Flight Watch: 122.0 FSS BOI: 122.2 / 122.6 KMAN ASOS:118.325 KEUL ASOS :135.07 KBOI ATIS:123.9 BOI App/Dep: North 126.9 / South 119.6 BOI Twr 118.1 / Gnd 121.7 |