| Cessna 182P Note: For N9989E Only v1.0 |
| --- |
| BEFORE TAKEOFF - Clearing circle for Pattern Traffic ( What is your ABORT Plan? Flaps UP or 20° ( Carb Heat OFF ( Transponder ALT ( Lights/Strobes ON ( Prop FWD ( Cowl Flaps OPEN ( Headset ON |
| TAKEOFF Normal: Rotate 60 MPH Vy 89 MPH (85 mph @ 10,000’) Short/Soft: Flaps 20° Vx 60 MPH (64 mph @ 10,000’) |
| CRUISE CLIMB 100 – 120 MPH BEST GLIDE 80 MPH (flaps up) |
| >1000’ AGL Oil Pres/Temp ( Ammeter ( Vacuum ( MP 15”- 23” ( Prop 2200 -2450 RPM |
| CRUISE ( Max 75% power ( Mixture LEAN to peak EGT, then ENRICH 125˚ rich of peak for Best power. ( Heading Indicator SET ( Cowl Flaps CLOSED ( Routinely Check Gauges:( Oil Press/Temp ( Ammeter ( Vacuum ( Landing Light OFF |
| LANDING ( Autopilot OFF ( Carb Heat ON ( Prop FWD ( Cowl Flaps CLOSED ( Fuel BOTH ( Mixture ENRICH ( Approach at 70-80 MPH |
| GO AROUND ( Full Throttle ( Pitch up ( Carb Heat OFF ( Flaps retract to 20° ( Climbing & above 80 MPH, retract flaps ( Cowl Flaps OPEN |
| AFTER LANDING Carb Heat OFF ( Transponder SBY ( Flaps UP Cowl Flaps OPEN ( Mixture LEAN for taxi |
| SHUTDOWN Avionics/Lights OFF ( Mixture OFF ( Master OFF ( Mags OFF Headset OFF ( Flight Plan Closed ( Control Lock Installed |
| POSTFLIGHT ( Hobbs Time RECORD ( Windows & Leading Edges CLEAN ( Wheel Chocks SET ( Seat Belts SECURE ( Interior CLEAN ( Airplane LOCKED ( Flight Log ENTERED ( Flight Plan CLOSED ( Hangar SECURE ( Padlock Set 0000 ( Lights OFF |
| MPH Vso 63 Vs1 68 Vfe 110 Va 2950 126 Va 2500 116 Va 2050 105 Vno 160 Vne 198 | Recommended Pattern Speeds/ Approx Pwr Settings Downwind: 90 - 100 mph / 16“ MP Abeam: 85 - 90 mph / 13“ MP Base: 80 - 85 mph / 13“ MP Final: 70 - 75 mph / 13“ MP (Full Flaps – No Flaps) |

Use at your own risk. The pilot must refer to the FAA approved documents for the correct information, and is responsible for safe operation of aircraft.

| Cessna 182P Note: For N9989E Only v1.0 |
| --- |
| PREFLIGHT Gust Lock - REMOVED Hobbs – Recorded. Enter flight into Flight Log System Autopilot - OFF Master – ON Flaps – 20° Fuel Gauges – Check Required Lights - CHECK Master – OFF Baggage Door – LOCKED Tires/Brakes – Press/Leaks (42 psi Main-49 psi Nose) Fuel Caps & Quantity Fuel Vents Oil level: 7 MIN / 8 MAX Qts. Oil filler cap - SECURE Nose strut Static Ports Wing Fuel Drains Engine Fuel Strainer START Seats – LOCKED Selt Belts – FASTEN Parking Brake – SET Passenger Briefing Cowl Flaps – OPEN Elevator & Rudder Trim - SET Fuel – BOTH Circuit Breakers – IN Avionics – OFF Mixture – RICH Prop – FWD Carb Heat – COLD Prime – As Required Throttle – open ½ Inch Clear Prop Master – ON Engage Starter (max 20 sec) | AFTER START Throttle – 1000 RPM Oil Pressure– in green < 30 seconds Flaps – UP Mixture – LEAN FOR TAXI Avionics – ON Beacon – ON Nav Lights – As Required Transponder – STBY RUNUP Doors & Windows – LATCHED Autopilot – TEST / Turn OFF Controls – Free & Correct Flaps – UP Trim – TAKEOFF Cowl Flaps – OPEN Fuel – BOTH Mixture – FULL RICH Throttle – 1700 RPM Mixture – BEST POWER Vacuum – Check (4.6”-5.4”) Mags(drop<150, difference ea <50) Prop – CYCLE 3X Carb Heat – TEST Alternator – TEST Throttle – 800-1000 RPM Instruments – CHECK Seat Belts – CHECK Flaps & Trims – CHECK COM – First Freqs 122.7 KMAN NAV – First Freqs OBS – SET Charts & Log – READY Headset – ON SEE OTHER SIDE FOR BEFORE TAKEOFF CHECK |

Emergency:  Com   121.5 / Squawk 7700

Loss Com.  Squawk 7600

Flight Watch: 122.0     FSS BOI: 122.2 / 122.6

KMAN ASOS:118.325    KEUL ASOS :135.07     KBOI ATIS:123.9

BOI App/Dep:  North 126.9 / South 119.6

BOI Twr 118.1 / Gnd 121.7