Use at your own risk. The pilot must refer to the FAA approved documents for the correct information, and is responsible for safe operation of aircraft.

| Cessna 182 v1.3 |
| --- |
| BEFORE TAKEOFF Flaps UP or 20° ( Carb Heat OFF ( Transponder ALT ( Lights/Strobes ON ( Prop FWD ( Cowl Flaps OPEN ( Headset ON |
| TAKEOFF Normal: Rotate 60 mph Vy 88 mph (84 mph @ 10,000’) Short/Soft: Flaps 20° Vx 61 mph |
| CRUISE CLIMB 100-120 mph BEST GLIDE 80 mph (flaps up) |
| >1000’ AGL Oil Pres/Temp ( Ammeter ( Vacuum MP 23” ( Prop 2450 RPM |
| CRUISE Max 75% power ( Mixture LEAN to peak EGT, then ENRICH Heading Indicator SET ( Cowl Flaps As Required Oil Press/Temp ( Ammeter ( Vacuum Landing Light OFF |
| LANDING Carb Heat ON ( Prop FWD ( Cowl Flaps CLOSED Fuel BOTH ( Mixture ENRICH Approach at 70-80 mph |
| GO AROUND Full Throttle ( Pitch up ( Carb Heat OFF ( Flaps retract to 20° Climbing & above 61 mph, retract flaps Cowl Flaps OPEN |
| AFTER LANDING Carb Heat OFF ( Transponder SBY ( Flaps UP Cowl Flaps OPEN ( Mixture LEAN for taxi |
| SHUTDOWN Avionics/Lights OFF ( Mixture OFF ( Master OFF ( Mags OFF Headset OFF ( Flight Plan Closed ( Control Lock Installed |
| POSTFLIGHT See checklist on other side |
| CAS MPH Vso 60 Vs1 67 Vfe 110 Va 128 Vno 160 Vne 193 |  |

Use at your own risk. The pilot must refer to the FAA approved documents for the correct information, and is responsible for safe operation of aircraft.

| Cessna 182 v1.3 |
| --- |
| PREFLIGHT Hobbs Master – ON Flaps – 20° Fuel Gauges – Check Exterior Lights - CHECK Interior Lights - CHECK Master – OFF Baggage Door – LOCKED Tires Fuel Caps & Quantity Fuel Vents Oil level – 9 qts min Oil filler cap - SECURE Nose strut Static Ports Wing Fuel Drains Engine Fuel Strainer START Seats – LOCKED Selt Belts – FASTEN Parking Brake – SET Cowl Flaps – OPEN Elevator & Rudder Trim - SET Fuel – BOTH Circuit Breakers – IN Avionics – OFF Mixture – RICH Prop – FWD Carb Heat – COLD Prime – As Required Throttle – ½” open Clear Prop Master – ON Engage Starter (max 30 sec) | AFTER START Throttle – 1000 RPM Oil Pressure – CHECK Flaps – UP Mixture – LEAN FOR TAXI Avionics – ON Beacon – ON Nav Lights – As Required Transponder – STBY RUNUP Doors & Windows – LATCHED Controls – Free & Correct Flaps – UP Trim – TAKEOFF Cowl Flaps – OPEN Fuel – BOTH Mixture – FULL RICH Throttle – 1700 RPM Mixture – BEST POWER Vacuum – Check (4.6”-5.4”) Mags (diff <50) Prop – CYCLE Carb Heat – TEST Alternator – TEST Throttle – 800-1000 RPM Instruments – CHECK Seat Belts – CHECK Flaps & Trims – CHECK COM – First Freqs NAV – First Freqs OBS – SET Charts & Log – READY Headset – ON SEE OTHER SIDE FOR BEFORE TAKEOFF CHECK |
| POSTFLIGHT Hobbs Time RECORD ( Windows & Leading Edges CLEAN Wheel Chocks SET ( Airplane LOCKED ( Hangar SECURE Padlock Set 0000 ( Lights OFF |