Use at your own risk. The pilot must refer to the FAA approved documents for the correct information, and is responsible for safe operation of aircraft.

| Cessna 172M – 160HP V1.1 |
| --- |
| BEFORE TAKEOFF - Clearing circle for Pattern Traffic Flaps UP ( Carb Heat OFF ( Transponder ALT Lights/Strobes ON ( Headset ON |
| TAKEOFF Do Not exceed 2500 RPM for more than 5 min during take-off Normal: Rotate 60 mph Vy 91 mph (85 mph @ 5,000’ DA) Short/Soft: Flaps 0 /10° Vx 68 mph |
| CRUISE CLIMB 90 mph RPM Do Not exceed 2500 RPM for more than 5 min during climb out BEST GLIDE 80 mph (flaps up) |
| >1000’ AGL Oil Pres/Temp ( Ammeter ( Vacuum ( Lights |
| CRUISE Do Not exceed 2500 RPM for more than 5 min during Cruse Landing Light OFF ( Mixture LEAN for max RPM Heading Indicator SET ( Routinely Check Gauges Oil Press/Temp ( Ammeter ( Vacuum ( Fuel ( Carb Temp (64R) |
| LANDING Carb Heat ON Fuel BOTH ( Mixture ENRICH Approach at 65-75 mph |
| GO AROUND Full Throttle ( Pitch up ( Carb Heat OFF Flaps retract to 20° ( Climbing & above 65 mph retract flaps |
| AFTER LANDING Carb Heat OFF ( Transponder SBY ( Flaps UP Mixture LEAN for taxi |
| SHUTDOWN Avionics/Lights OFF ( Mixture OFF ( Master OFF ( Mags OFF ( Headset OFF ( Parking Brake SET Control Lock Installed ( Flight Plan Closed |
| POSTFLIGHT Hobbs Time RECORD ( Windows & Leading Edges CLEAN Wheel Chocks SET ( Airplane LOCKED ( Hangar SECURE Padlock Set 0000 ( Lights OFF |
| CAS MPH Vso 54 Vs1 61 Vfe 100 Va 112 Vno 145 Vne 182 | Recommended Pattern Speeds / Approximate Power settings. Downwind: 90 mph / 2000 RPM Abeam: 85 mph / 1500 RPM / 10 flaps Base: 80 mph / 1500 RPM / 20 flaps Final: 70 mph / 1500 RPM / 30 – 40 flaps |

Use at your own risk. The pilot must refer to the FAA approved documents for the correct information, and is responsible for safe operation of aircraft.

| Cessna 172M – 160HP V1.1 |
| --- |
| PREFLIGHT Hobbs Master – ON Flaps – 20° Fuel Gauges – Check Exterior Lights - CHECK Interior Lights - CHECK Master – OFF Baggage Door – LOCKED Tires Fuel Caps & Quantity Fuel Vents Oil level – 6 qts min Nose strut Static Port Wing Fuel Drains Engine Fuel Strainer START Seats – LOCKED Selt Belts – FASTEN Parking Brake – SET Fuel – BOTH Circuit Breakers – IN Avionics – OFF Mixture – RICH Carb Heat – COLD Prime – As Required Throttle – OPEN ½” Clear Prop Master – ON Engage Starter (max 30 sec crank if no start) | AFTER START Throttle – 1000 RPM Oil Pressure – CHECK Flaps – UP Mixture – LEAN FOR TAXI Avionics – ON Beacon – ON Nav Lights – As Required Transponder – STBY RUNUP Doors & Windows – LATCHED Controls – Free & Correct Flaps – UP Trim – TAKEOFF Fuel – BOTH Mixture – FULL RICH Throttle – 1700 RPM Mixture – BEST POWER Vacuum – Check (4.6”-5.4”) Mags ( drop < 125, diff <50) Carb Heat – TEST Alternator – TEST Throttle – 1000 RPM Instruments – CHECK Seat Belts – CHECK COM – First Freqs NAV – First Freqs OBS – SET Charts & Log – READY Headset – ON SEE OTHER SIDE FOR BEFORE TAKEOFF CHECK |
| Emergency: Com 121.5 / Squawk 7700 Loss Com. Squawk 7600 Flight Watch: 122.0 FSS BOI: 122.2 / 122.6 EUL ASOS : 135.07 BOI ATIS: 123.9 BOI App/Dep: North 126.9 / South 119.6 BOI Twr 118.1 / Gnd 121.7 |