## Slide 1: GARMIN EspTM
(ELECTRONIC STABILITY & PROTECTION)

## Slide 2: Let’s break the ice…
I told my friend 10 jokes to make him laugh.
Sadly, no pun in ten did.

## Slide 3: Introductions
Background
  Started flying in the Army
  Active CFII
    TVCC
Flying Experience
  Commercial, ASEL, AMEL
  CFI, MEI
Jeff Norris

## Slide 4: Session contents
ESP
Smart Glide
Differences in T-Craft tail numbers
Videos and in-Flight Scenario

## Slide 5: references?
https://www.t-craft.org/documents/fleet/G3X.manual.pdf
https://www.t-craft.org/documents/fleet/G5Manual.pdf https://www.t-craft.org/documents/fleet/GFC500.pdf
https://www.t-craft.org/documents/fleet/G5-GFC500Basics.pdf
Pages 69-74
Pages 284-289

## Slide 6: What are my references?
AFMS GFC 500 AUTOPILOT in Textron 172 Series
https://www.t-craft.org/documents/fleet/G5Manual.pdf https://www.t-craft.org/documents/fleet/GFC500.pdf
https://www.t-craft.org/documents/fleet/G5-GFC500Basics.pdf
Pages 69-74
Pages 284-289

## Slide 7: Why this matters (practical scenarios)
Changes control feel & response
Alters how the airplane will recover from small deviations
Creates mode-awareness and startle risk
Reduces workload (when used correctly)
Affects training goals
Notes: 1. ESP can oppose or damp pilot inputs. If you don’t know it’s active, your inputs may feel “mushy,” light, or resisted – or conversely, when ESP disengages the airplane will suddenly feel different.
2. ESP will help prevent small exceedances; beginner pilots may get saved from a small mistake, which is good — but that same “help” can mask poor scanning or energy management if not trained properly.
3. ESP will help prevent small exceedances; beginner pilots may get saved from a small mistake, which is good — but that same “help” can mask poor scanning or energy management if not trained properly.
4. In IMC, turbulence, or high workload single-pilot IFR ops, ESP provides automatic stability corrections that reduce pilot workload and help maintain control.
5. Instructors must decide when to practice maneuvers with ESP ON (to train automation management) vs. OFF (to train raw stick-and-rudder skills).

## Slide 8: Garmin electronic stability & Protection (esptm)
Provides safety enhancements to aid pilots against loss of control situations
Intended to help alert and assist pilots when operation outside the normal flight envelope occurs
Can be disabled or overridden at any time
Notes: 1. ESP is an optional feature.
2. ESP is intended to monitor the aircraft and provide control input feedback when necessary to discourage operating the aircraft at potentially unsafe attitudes and/or airspeeds.

## Slide 9: Garmin electronic stability & Protection (esptm)
ESP functions when the aircraft meets the following:
  In flight
  Above 500 ft AGL – automatically arms
  Below 200 ft AGL – automatically disarms
  Autopilot not engaged
Notes: If enabled, this feature will automatically arm when the aircraft is above 500 feet AGL and the autopilot is not engaged, and disarm when below 200 feet AGL.

## Slide 10: Garmin electronic stability & Protection (esptm)
System is enabled and monitoring flight parameters when the double lines are present at the 45⁰ point on the roll scale

## Slide 11: Garmin electronic stability & Protection (esptm)
ESP will engage whenever the aircraft exceeds one or more conditions beyond the normal flight envelope:
  Pitch
  Roll
  VNE
  Impending stall

## Slide 12: Garmin electronic stability & Protection (esptm)
ESP will provide force to the appropriate control surface to return the aircraft to the normal flight envelope
The pilot will perceive resistance to control movements in the undesired direction as the aircraft approaches a steep attitude, high airspeed, or impending stall
The pilot can override by pressing the Control Wheel Steering or Autopilot Disconnect Switch
When switches are released, forces will again be applied

## Slide 13: Level Mode
As an additional protective feature, ESP will automatically turn on the autopilot after a period of normal flight envelope excursion.
After 10 seconds of ESP engagement (cumulative; not necessarily consecutive seconds) of a 20-second interval, the autopilot will engage automatically with the flight director in Level (LVL) mode
This feature could be helpful during situations like spatial disorientation or pilot incapacitation
Notes: The G5 manual says, “the autopilot can be configured to engage with the flight director in Level Mode, bringing the aircraft into level flight. An aural “Engaging Autopilot” alert is played and the flight director mode annunciation will indicate ‘LVL’ for vertical and lateral modes.” T-Craft G5 Manual digital page 82, manual page 70.

## Slide 14: Roll engagement
As roll attitude exceeds the configured limit, ESP will engage and the Roll Limit Indicators will move to 15º less than the configured ESP bank limit.
The Roll Limit Indicator now indicates where ESP will disengage as roll attitude decreases.
Notes: ROLL ENGAGEMENT Roll Limit Indicators displayed on the roll scale are configurable between 45º and 60º right and left, indicating where ESP will engage. As roll attitude exceeds the configured limit, ESP will engage and the Roll Limit Indicators will move to 15º less than the configured ESP bank limit. The Roll Limit Indicator now indicates where ESP will disengage as roll attitude decreases.

## Slide 15: Differences between esp bank operating ranges:
Notes: There is a difference between our T-Craft G3X and G5 ESP Operating Range when engaged and the G1000 NXi. Compare Garmin G1000 NXi Pilot’s Guide for the Cessna Nav III, and aircraft such as Cessna Caravan, Piper Archer
In Garmin G1000 Nxi aircraft, the maximum ESP Bank range is +/-75⁰

## Slide 16: Differences between esp pitch operating ranges:
Notes: In Garmin G1000 Nxi aircraft, the maximum ESP pitch range is +/-50⁰. Don’t be confused: in our T-Craft Airplanes, the there is no disengagement at +/-50⁰ pitch.

## Slide 17
ESP triggered at 45⁰ Bank
ESP triggered at 45⁰ Bank
ESP Roll Limits:

## Slide 18
ESP Pitch Limits:
ESP triggered at:
  Xx⁰ Pitch C172
  Xx⁰ Pitch C182
ESP triggered at:
  Xx⁰ Pitch C172
  Xx⁰ Pitch C182

## Slide 19: AIRSPEED PROTECTION IN G3X:
NOTE: If AGL height data is unavailable (i.e., GPS altitude or terrain data is unavailable), low-airspeed protection is not supported.
An airspeed below the minimum configured airspeed or above maximum configured airspeed will result in ESP applying force to raise or lower the nose of the aircraft.
When the high or low airspeed condition is remedied, ESP force is no longer applied.
An audible "Airspeed" alert may be configured.

## Slide 20: AIRSPEED PROTECTION:
High Airspeed Protection
  Exceeding VNE will result in ESP applying force to raise the nose
Low Airspeed Protection (Cessna 172)
  When airspeed decelerates below 55 KIAS and remains there for 1 second ESP will engage and apply nose down force
Low Airspeed Protection (Cessna 182)
  When stall warning has been active for at least a half second, ESP will engage and apply nose down force.

## Slide 21: Esp warnings
Notes: A couple overall warnings that we have and these are straight out of the aircraft flight manual supplements don’t
try to overpower the the autopilot this can create massive opposing trim forces so when we do disconnect
now we're going to massively retrim the aircraft.

## Slide 22: Another warning
Notes: Don't attempt to re-engage an autopilot or use the manual manual electric
trim until the cause of the malfunctions been corrected generally speaking grab the controls firmly,
disconnect the autopilot, whether it’s through ap disconnect, pressing the 507, or pulling a circuit breaker. If
you have an issue of a massive failure in flight don't probably best but don’t
re-engage it fly the aircraft get it on the ground now we can start trouble shooting it when we're safe

## Slide 23: PITCH ENGAGMENT IN G3X:
Notes: ESP pitch engagement is configurable between 10º and 25º nose-up and between 5º and 25º nose-down. Once engaged, the torque applied by ESP is at its maximum when pitch is 5º more than the configured nose-up and nose-down pitch limits, and tapers to the minimum applied torque when pitch is 5º less than the configured noseup and nose-down pitch limits. When beyond 5º of the configured pitch limit, the maximum torque is held until the aircraft returns inside the protected envelope. The opposing force increases or decreases depending on the pitch angle and the direction of pitch travel. This force is intended to encourage movement in the pitch axis in the direction of the normal pitch attitude range for the aircraft. The presence of yellow chevrons indicate that ESP is engaged in these nose-up/ nose-down conditions.

## Slide 24: Level Mode
Note: ESP will be automatically enabled prior to each flight and should be turned off prior to attempting training maneuvers that exceed ESP envelope limits, i.e:
  Steep turns
  Slow flight
  Stalls
  Unusual attitude recoveries, etc…
ESP may be re-enabled after training maneuvers are complete

## Slide 25: Next an esp overview video…
Overview of Electronic Stability and Protection

## Slide 27: Next a video on esp…
Understanding Electronic Stability and Protection

## Slide 29: In c172, EnaBLING/DISABLING ESP USING THE G5 MENU:
1) From the PFD Page, press the Selection Knob to display the Menu.
2) Turn the Selection Knob to highlight ESP.
3) Press the Selection Knob to enable or disable ESP.

## Slide 30: In c172, underspeed and overspeed protection (USP/OSP):

## Slide 31: In c172, esp specifics:

## Slide 32: In c182, underspeed and overspeed protection (usp/osp):

## Slide 33: In c182, esp specifics:

## Slide 34: Enabling/disabling esp using the g3x:
Using the G3X Touch Autopilot Interface:
  1) From the PFD, touch the Autopilot Status Box. The Automatic Flight Control System page is displayed.
    Or:
  From the Main Menu, touch Flight Controls.
  2) Touch the ESP button on the Automatic Flight Control System page to enable/disable ESP.
ESP can be configured to be automatically enabled when starting the system.
Notes: ROLL ENGAGEMENT Roll Limit Indicators displayed on the roll scale are configurable between 45º and 60º right and left, indicating where ESP will engage. As roll attitude exceeds the configured limit, ESP will engage and the Roll Limit Indicators will move to 15º less than the configured ESP bank limit. The Roll Limit Indicator now indicates where ESP will disengage as roll attitude decreases.

## Slide 37: Check on Learning:
Which T-Craft aircraft have Smart Glide?
  All C172’s and C182’s, not C152
  N1293F, N9989E, N7593S, N121M
Which aircraft have ESP?
  N1293F and all C182s
Which aircraft have a GFC-500?

## Slide 38: Check on learning:
15 degrees more than the configured bank limit (and tapers to the minimum applied torque when the bank angle is 15 degrees less than the configured bank limit.
Once ESP is engaged, when is the maximum torque applied?

## Slide 39: Bonus question:
In the G-5, at what positive and negative pitches does the PFD pitch ladder turn red?
Notes: Positive 60 and negative 40
When the aircraft enters an unusual pitch attitude, red extreme pitch warning chevrons pointing toward the horizon are displayed on the attitude indicator starting at 60 degrees above and 40 degrees below the horizon line.
Reference:
https://static.garmin.com/pumac/190-01112-12_01.pdf

## Slide 40: More Resources
Understanding Garmin Electronic Stability and Protection (ESP™)
https://www.youtube.com/watch?v=5F4hduLn9Xs
Getting to Know the Garmin GFC™ 500 Autopilot – Garmin Training
https://www.youtube.com/watch?v=nQMWC5Aq1JM
GFC 500 Autopilot Video
https://www.t-craft.org/documents/zoom/9.29.22.Safety.Presentation.GFC500.Pete_Glick.mp4
www.flygarmin.com/training

## Slide 41: esp summary
Questions
Feedback
Thanks to Pete and the board

## Slide 42: Thank You
info@westernidahoaviation.com